## Slide 1
Design a Don't-Touch-Me robot which says "DO NOT TOUCH ME" and try to run away when attempted to touch it. 1. When touched, the robot yells "DO NOT TOUCH ME" (at least urgent sound to indicate) or runs away. 2. The robot counts the number of times being touched and display it with LED display device, like Digital tube. 3. The robot gets angry when the number hits a threshold value. (The behavior of "getting angry" can be defined by ourselves.)
INTRODUCTION & ABSTRACT
Simulation
IMPLEMENTATION
Thanks for our TA : 苏隽岩
Counting Module
  555Timer
  Capacitor: 1uF, 33uF
  Resistor: 1kΩ * 7, 510kΩ
  Counter: CD4518
  Encoder: CD4543
  7-Seg LED Nixietube: 5611AH
  Electric relay
Angry Module
  And Gate
  555Timer
  Capacitor: 1uF * 2
  Resistor: 510kΩ, 50kΩ, 1kΩ, 2kΩ
  Counter: CD4017
  LED * 7
  Electric relay
  Resistor: 1kΩ
When Distance-Measure Module is triggered (Dark), robot will move forward and the recording number plus one. When the times of being triggered adds to 7, it will trigger the Voice Module and Angry Module. Robot yells "Don't touch me!", and the horse race lamp starts to work.
Shanghaitech University SIST EE111 Project 7
梁家伟 姚进
Don’t-Touch-Me Robot
Block schematic
Components
Distance-Measure Module: We use photoelectric resistor and relay to build a photo switch circuit. The trigger signals controls motion module, which makes robot move forward.
Counting Module: We use CD4518 as counter, which is a Decimal Adder. It can represent "0~9" by 4-bit binary numbers, and showed by the level of output voltage. Since it only accept SQUARE WAVE SIGNAL, We use 555Timer to solve this problem. After that, we use CD4543 as encoder. Encodes 4-bit-number into 7 outputs, and connect them to 7-Seg LED Nixie tube (Common cathode) to show numbers in a readable way.
Angry Module: We use AND gate to check the binary threshold number. Its output signal is connected to voice module (recording module) and a horse race lamp constructed by a 555Timer and Counter CD4017.
Distance-Measure Module
  Photoelectric relay
  Battery * 8 (12V)
Motion Module and Voice Module
  Battery * 3 (4.5V)
  Electric motor * 2
  Electric relay
  Recording Module
General
  Battery * 3 (4.5V)
Result